## Slide 1: VLSI DSP Final Project MIMO Detection Algorithms Comparison and Analysis
Team members: 310513008 楊士緯, M093799 鄭宇倫
June 6th, 2022

## Slide 2: Outline
Introduction
System Model
MIMO detection algorithm
  ML detector
  ZF detector
  MMSE detector
  K-best detector
Simulation results
Conclusion
References

## Slide 3: Outline
Introduction
System Model
MIMO detection algorithm
  ML detector
  ZF detector
  MMSE detector
  K-best detector
Simulation results
Conclusion
References

## Slide 4: Introduction (1/2)
A communication system is composed of transmitter, receiver, and channel
In multiple-input multiple-output (MIMO) communication system
  Both the transmitters and the receivers are equipped with several antennas
  Which will help in achieving high gains in spectral, power, and energy efficiency
The hardware implementation of MIMO detector is an important issue [1]
  As the scale of the system getting larger to deal with the 5G technologies
Optimal MIMO detector such as maximum likelihood detector is
  Infeasible due to its high computational complexity
Low computational complexity algorithm achieving near-optimal performance is required
  Linear detectors [2], tree-based-search detectors [3][4] are used to deal with MIMO detection

## Slide 5: Introduction (2/2)
In this project, we comparison the performance and complexity of some algorithms mentioned above
  Maximum likelihood, zero forcing, minimum mean square error, and K-best
A simulation platform was built to implement the MIMO detection algorithm
  A 2X2 MIMO system with QPSK modulation
2X2 MIMO system
MIMO
detector

## Slide 6: Outline
Introduction
System Model
MIMO detection algorithm
  ML detector
  ZF detector
  MMSE detector
  K-best detector
Simulation results
Conclusion
References

## Slide 7: System Model (1/2)
  x is the input vector
  y is the output vector
  H is the channel matrix
  n is noise
Noise

## Slide 8: System Model (2/2)
In our system
  The input antenna number (N) is 2
  The output antenna number (M) is 2
  The modulation is QPSK (4-QAM)
  With an additive Gaussian white noise
  Channel matrix size : 2X2
  The signal length is 1024
Channel matrix H can obtain by
  Channel Model
    Ex: in slow and flat fading case, the channel matrix element typically assumed i.i.d. Rayleigh distributed
  Sampling : Channel State Information (CSI)
Performance comparison criterion
  Signal-to-noise ratio (SNR), bit error rate (BER)
1+j
-1+j
-1-j
1-j

## Slide 9: Outline
Introduction
System Model
MIMO detection algorithm
  ML detector
  ZF detector
  MMSE detector
  K-best detector
Simulation results
Conclusion
References

## Slide 10: ML Detector
The optimum detector
  S: symbol set
  K: sample size
The complexity grows exponentially with the number of the antenna
  4 symbols, 1 antenna – S=4
  4 symbols, 2 antenna – S=16
Symbol set |  |  | 
1+j | 1-j | -1+j | -1-j

## Slide 11: ZF Detector
Linear detector
Noise enhancement would be serious if H is ill-conditioned
Effected of ill-conditioned channel
  Decision regions of detector have been twisted by H
  With ZF detector adopted, transformed noise would be seriously enhanced
    Making decision easily wrong

## Slide 12: MMSE Detector
Linear detector
The solution:
Jointly consider channel and noise effects
Better performance than ZF detector

## Slide 13: K-Best Detector (1/3)
Tree-search based detector (breadth-first search)
Preprocessing using QR decomposition
  Q is an unitary matrix
  R is an upper triangular matrix
The objective function is written as
d means the partial Euclidean distance (PED)
K-best keep K nodes with minimum PED in each layer

## Slide 14: K-Best Detector (2/3)
For K=2
Path1
Path2
Path |  | 
Path1 | 1 + j | 1 + j
Path2 | - 1 - j | 1 + j
Path |  | 
Path1 | 1 + j | 1 + j
Path2 | - 1 - j | 1 + j

## Slide 15: K-Best Detector (3/3)
For K=4
Path1
Path2
Path3
Path4
Path |  | 
Path1 | 1 + j | 1 + j
Path2 | - 1 - j | 1 + j
Path3 | - 1 + j | 1 - j
Path4 | 1 - j | - 1 - j
Path |  | 
Path1 | 1 + j | 1 + j
Path2 | - 1 - j | 1 + j
Path3 | - 1 + j | 1 - j
Path4 | 1 - j | - 1 - j

## Slide 16: Outline
Introduction
System Model
MIMO detection algorithm
  ML detector
  ZF detector
  MMSE detector
  K-best detector
Simulation results
Conclusion
References

## Slide 17: Simulation Results (1/4)
Detection results

## Slide 18: Simulation Results (2/4)
Noise enhancement problem in ZF detector

## Slide 19: Simulation Results (3/4)
BER performance comparison

## Slide 20: Simulation Results (4/4)
Detector | BER | Complexity | Type
ML | Optimal | Dramatically complex | 
ZF | Very poor | Very simple | Linear detector
MMSE | Poor | Simple | Linear detector
K-best | Good | Rather complex | Tree-based-search detector (breadth first search)
Complexity analysis
Summary of all detectors

## Slide 21: Outline
Introduction
System Model
MIMO detection algorithm
  ML detector
  ZF detector
  MMSE detector
  K-best detector
Simulation results
Conclusion
References

## Slide 22: Conclusion
From the simulation results, we can found the disadvantage of ZF detector
  Noise enhancement problem may influence the detection results seriously
For the linear detector
  ZF is the best linear detector regarding SNR criterion
  MMSE is the best linear detector regarding SINR criterion
For the K-best detector
  Has a higher performance than linear detector but also a higher complexity
The value of K in K-best detector is an important issue
  Since the value of K is a tradeoff between BER and complexity
K-best detector is a more flexible choice than ZF and MMSE for MIMO system and VLSI implementation

## Slide 23: References
[1] Trotobas, B.; Nafkha, A.; Louët, Y. A.; Louët, Y. A review to massive MIMO detection algorithms: Theory and implementation. In Advanced Radio Frequency Antennas for Modern Communication and Medical Systems; IntechOpen: London, UK, 2020.
[2] Wübben, D. Seethaler, J. Jaldén, and G. Matz, “Lattice reduction,” IEEE Signal Processing Mag., vol. 1, no. 3, pp. 70‐91 May 2011.
[3] Burg, “VLSI circuit for MIMO communication systems,” Ph.D. dissertation, Swiss Federal Institution of Technology Zurich, 2006.
[4] I. A. Bello, B. Halak, M. El-Hajjar and M. Zwolinski, "VLSI implementation of a scalable K-best MIMO detector," 2015 15th International Symposium on Communications and Information Technologies (ISCIT), 2015.

## Slide 24
Thank you！